## Slide 1: William Stallings Computer Organization and Architecture 10th Edition

## Slide 2: Chapter 18
Multicore Computers

## Slide 4
Power
Memory
Pollack’s rule states that performance increase is roughly proportional to square root of increase in complexity.

## Slide 5
overhead is a result of communication and distribution of work among multiple processors and as a result of cache coherence overhead

## Slide 7: Effective Applications for Multicore Processors
Multi-threaded native applications
  Thread-level parallelism
  Characterized by having a small number of highly threaded processes
Multi-process applications
  Process-level parallelism
  Characterized by the presence of many single-threaded processes
Java applications
  Embrace threading in a fundamental way
  Java Virtual Machine is a multi-threaded process that provides scheduling and memory management for Java applications
Multi-instance applications
  If multiple application instances require some degree of isolation, virtualization technology can be used to provide each of them with its own separate and secure environment

## Slide 8
Earlier multicore chips, still seen in embedded chips
No on-chip cache sharing
(eg) AMD Opteron
Similar allocation of chip space is to memory, but shared L2 cache
(eg) Intel Core Duo
(eg) Core i7
Intel Core Duo uses superscalar cores, whereas the Intel Core i7 uses SMT cores. SMT has the effect of scaling up the number of hardware- level threads that the multicore system supports.

## Slide 9: Heterogeneous Multicore Organization
Refers to a processor chip that includes more than one kind of core
The most prominent trend is the use of both CPUs and graphics processing units (GPUs) on the same chip
This mix however presents issues of coordination and correctness
GPUs are characterized by the ability to support thousands of parallel execution threads
Thus, GPUs are well matched to applications that process large amounts of vector and matrix data

## Slide 11
Table 18.1
Operating Parameters of AMD 5100K
Heterogeneous Multicore Processor
FLOPS = floating point operations per second
FLOPS/core = number of parallel floating point operations that can be performed

## Slide 12: Example CPU and GPU
 | CPU Intel core i7-6700K(2015) | GPU NVIDIA GTX 1080(2014) | 
# of core | 4 | 40 | # of SM
# of threads | 8 | 2560 | 
# of FP64 | 4*8(32) | 40*2(80) | 
# of FP32 | 4*16(64) | 40*64(2560) | 
# of FP16 | no | 40*64(2560) | 
Peek FP32 performance | 512GFlops | 8228GFlops | 
On-chip memory | 8MB | 2MB | LLC
Off-chip memory bandwidth | 34.1 GB/s | 320 GB/s | 
Clock | 4(4.2)GHz | 1.607(1.733)GHz | 
Power | 91W | 180W | 

## Slide 13: Example CPU and GPU
SM : Steaming Multiproceesor
i7 CPU includes embedded GPU
10 GPU includes GDDR5X
  a high bandwidth ("double data rate") interface designed for use in graphics cards, game consoles, and high-performance computation.

## Slide 14: SIMD < SIMT < SMT: parallelism in NVIDIA GPUs
In SIMD, elements of short vectors are processed in parallel.
In SMT, instructions of several threads are run in parallel.
SIMT is somewhere in between – an interesting hybrid between vector processing and hardware threading.
  the trade-off between flexibility and efficiency
  multiple independent threads execute concurrently using a single instruction.
  In GPGPU, SIMT is a better choice

## Slide 16: Heterogeneous System Architecture (HSA)
Key features of the HSA approach include:
  The entire virtual memory space is visible to both CPU and GPU
  The virtual memory system brings in pages to physical main memory as needed
  A coherent memory policy ensures that CPU and GPU caches both see an up-to-date view of data
  A unified programming interface that enables users to exploit the parallel capabilities of the GPUs within programs that rely on CPU execution as well
  The overall objective is to allow programmers to write applications that exploit the serial power of CPUs and the parallel-processing power of GPUs seamlessly with efficient coordination at the OS and hardware level

## Slide 17: Dark silicon – is the end of multicore?
The idea is, you can have 2x more cores with each lithography shrink, but your energy efficiency grows only by a square root of 2.
So 4 shrinks mean 16x more cores – but within a fixed power budget, you can only actually use 4. So progress slows down!
Gaining more than 4x has always been possible with specialized cores, of course; dark silicon is just a compelling reason to do it, because it robs you of the much easier alternative.

## Slide 19
The A15 is designed for maximum performance within the mobile power budget. The A7 processor is designed for maximum efficiency and high enough performance to address all but the most intense periods of work (aimed at the smartphone and tablet market)
A7 cores: background tasks (playing music, sending texts, phone calls)
A15 cores : high intensity tasks (video, gaming, navigations)

## Slide 22: Cache Coherence
May be addressed with software-based techniques
  Software burden consumes too many resources in a SoC chip
When multiple caches exist there is a need for a cache-coherence scheme to avoid access to invalid data
There are two main approaches to hardware implemented cache coherence
  Directory protocols
  Snoopy protocols
  ACE (Advanced Extensible Interface Coherence Extensions)
  Hardware coherence capability developed by ARM
  Can be configured to implement whether directory or snoopy approach
  Has been designed to support a wide range of coherent masters with differing capabilities
  Supports coherency between dissimilar processors enabling ARM big.Little technology
  Supports I/O coherency for un-cached masters, supports masters with differing cache line sizes, differing internal cache state models, and masters with write-back or write-through caches

## Slide 23
OWNED: the exclusive right to make changes. It must broadcast those changes to all other caches sharing the line. The introduction of owned state allows dirty sharing of data, i.e., a modified cache block can be moved around various caches without updating main memory.

## Slide 24
(Table can be found on page 676 in the textbook.)
When in Exclusive or Modified, and other cache reads

## Slide 27: Interrupt Handling
Generic interrupt controller (GIC) provides:
Masking of interrupts
Prioritization of the interrupts
Distribution of the interrupts to the target A15 cores
Tracking the status of interrupts
Generation of interrupts by software
GIC
Is memory mapped
Is a single functional unit that is placed in the system alongside A15 cores
This enables the number of interrupts supported in the system to be independent of the A15 core design
Is accessed by the A15 cores using a private interface through the SCU(Snoop Control Unit)

## Slide 28: GIC
Designed to satisfy two functional requirements:
Provide a means of routing an interrupt request to a single CPU or multiple CPUs as required
Provide a means of interprocessor communication so that a thread on one CPU can cause activity by a thread on another CPU
Can route an interrupt to one or more CPUs in the following three ways:
An interrupt can be directed to a specific processor only
An interrupt can be directed to a defined group of processors
An interrupt can be directed to all processors

## Slide 29: Interrupts can be:
Inactive
  One that is nonasserted, or which in a multiprocessing environment has been completely processed by that CPU but can still be either Pending or Active in some of the CPUs to which it is targeted, and so might not have been cleared at the interrupt source
Pending
  One that has been asserted, and for which processing has not started on that CPU
Active
  One that has been started on that CPU, but processing s not complete
  Can be pre-empted when a new interrupt of higher priority interrupts A15 core interrupt processing
Interrupts come from the following sources:
  Interprocessor interrupts (IPIs)
  Private timer and/or watchdog interrupts
  Legacy FIQ line (bypasses the Interrupt Distributor logic and directly drives interrupt requests into the CPU)
  Hardware interrupts

## Slide 31: Cache Coherency
Snoop Control Unit (SCU) resolves most of the traditional bottlenecks related to access to shared data and the scalability limitation introduced by coherence traffic
L1 cache coherency scheme is based on the MESI protocol
Direct Data Intervention (DDI)
  Enables copying clean data between L1 caches without accessing external memory
  Reduces read after write from L1 to L2
  Can resolve local L1 miss from remote L1 rather than L2
Duplicated tag RAMs
  Cache tags implemented as separate block of RAM
  Same length as number of lines in cache
  Duplicates used by SCU to check data availability before sending coherency commands
  Only send to CPUs that must update coherent data cache
Migratory lines
  Allows moving dirty data between CPUs without writing to L2 and reading back from external memory

## Slide 34: Summary
Hardware performance issues
  Increase in parallelism and complexity
  Power consumption
Software performance issues
  Software on multicore
  Valve game software example
  Intel Core i7-990X
  IBM zEnterprise EC12 mainframe
  Organization
  Cache structure
Multicore organization
  Levels of cache
  Simultaneous multithreading
  Heterogeneous multicore organization
  Different instruction set architectures
  Equivalent instruction set architectures
  Cache coherence and the MOESI model
  ARM Cortex-A15 MPCore
  Interrupt handling
  Cache coherency
  L2 cache coherency
Chapter 18
Multicore
Computers